## Slide 1: Smart neighborhood system for shutters management
Baraldi Francesco, Pagliani Matteo

## Slide 2: Outline
Introduction
Architecture
Prototype specifications
Reinforcement learning approach

## Slide 3: Introduction

## Slide 4: Introduction
Too lazy to close the shutters in case of a thunderstorm?
Do you often forget to close the shutters before falling asleep?
Or do your flowers need sunlight when you are on holiday away from home?
 This system is the answer for you! Our product automatically open or close the shutters of houses depending on weather conditions. Its scalability allows it to be used not only by you, but also by your neighbours, aiming to control the shutters of several houses in your neighbourhood simultaneously.

## Slide 5: How to use
You don’t have to worry about anything, the system takes care of your house for you:
When specific weather conditions trigger our system, it will take a decision about closing or opening the shutters in total autonomy. You will be notified directly on your smartphone when a decision is taken, and you can feed back if you liked that decision or not, giving us the possibility to improve based on your habits! The system learns how to perfectly fit your needs
When you are away, you can always control the shutters remotely via web
Obviously, you can control the shutters manually thanks to specific buttons installed in your house
The system takes into account your neighbours action to make better decisions on your own windows

## Slide 6: Composition of the kit
The kit is composed by:
1 internal kit per house: a microcontroller, an actuator and a button for each of the windows you want to control
1 external kit per neighbourhood: some sensors (a photoresistor and a wind speed sensor) and a control unit for the whole neighbourhood, which will be installed in a strategic position close to the houses to be managed
Finally you shall install the Telegram application on your smartphone and keep on hand the web site for optimal control.

## Slide 7: Key points: why chosing our system?
Because it is:
Easy to setup
Not invasive
Automatic: the system can work completely autonomously
Flexible/modular:
Scalable: multiple windows in a house, multiple houses in a neighborhood, multiple neighborhoods
Adaptive to users’ habits  AI approach

## Slide 8: Architecture

## Slide 9: Architecture: real model

## Slide 10: Architecture: prototype

## Slide 11: Prototype specifications

## Slide 12: Real model vs prototype
Real Model | Prototype
1 Arduino Nano for each window | 1 Arduino UNO Rev.3 for two windows
1 Raspberry Pi for each house which manages all the house’s windows and runs the internal bridge | Laptop as internal bridge
1 Raspberry Pi for each neighborhood that runs the external bridge | Laptop as external birdge
Server Django and engine hosted with a public IP | Server Django and engine running in localhost
Prettier buttons | Push buttons
1 custom actuator for each window | 1 servomotor for each window (Hitec and TowerPro)
Wind speed sensor | 1 potentiometer as wind speed sensor
Proper web app frontend for improved UE | Simple web app using Django template
Deep Reinforcement Learning decision logic to manage all possible combinations of states | Hard-coded decision logic and neighbours “control” in case of uncertain situations

## Slide 13: Connection schemas
The Arduino Uno for the internal kit is connected to:
1 Hitec servomotor
1 TowerPro servomotor
2 push buttons

## Slide 14: Connection schemas (1)
The Arduino Uno for the external kit is connected to:
1 photoresistor
1 potentiometer

## Slide 15: FSM for push buttons
States: {S0, S1, S2}
  S0: initial state
  S1: button pressed
  S2: button pressed more than one time consecutively
Inputs: {PRESSED, RELEASED}
  PRESSED : high (5V) digital signal due to the button pression
  RELEASED : low (0V) digital signal due to the button release
Outputs: {MOVE, NOT_MOVE}
  MOVE: allows the servo to change the state of the window (from open to closed or viceversa)
  NOT_MOVE: does not allow the servo to change the state of the window

## Slide 16: Code tables for serial communication between «internal» Arduino and its bridge
0xFF | 0x01 | WINDOW_PIN | 0xFE
Header | Payload length | Payload | Footer
Header (1 byte): identifies the beginning of the packet
Payload length (1 byte): specifies the byte length of the payload
Payload (1 byte): the microcontroller writes on the serial bus the number of the pin connected to the servomotor whose window has just changed state. The bridge will read from the serial and will update accordingly in the database the state of the window.
Footer (1 byte): identifies the end of the packet

## Slide 17: Code tables for serial communication between «external» Arduino and its bridge
0xFF | 0x02 | Potentiometer value | Photoresistor value | 0xFE
Header | Payload length | Payload | Payload | Footer
Header (1 byte): identifies the beginning of the packet
Payload length (1 bytes): specifies the byte length of the payload
Payload (2 byte): the first and the second byte are respectively the value read by the potentiometer and the value read by the photoresistor, both mapped from the original range 0 – 1024, to the range 0 – 253 in order to store them in exactly one byte
Footer (1 byte): identifies the end of the packet

## Slide 18: Web App – Login Page

## Slide 19: Web App – Home Page

## Slide 20: Telegram bot
A Telegram bot called smart_neighborhood is used to notify the house’s owners whenever the system decides to move the windows. The bot has two simple commands:
/start, that is automatically called when the bot is started, gives a welcome message and store, if new, the user in the database;
/help, which gives a short description of bot’s functionalities.
When the engine decides to move the windows, it calls a specific function of the bot which sends a message to all the chat IDs stored in the database in order to make the owners aware of the new state of their windows. In the message, it is also suggested to use the web app to change the state of the windows if the new state does not match the user’s will.

## Slide 21: SqLite3 database structure

## Slide 22: SqLite3 database structure (1)
The database is automatically managed by Django using the model part of the MVC approach: we define a python class for each DB table and Django creates the respective relational DB. The 4 classes are described below:
ChatTelegram: it represents a Telegram chat identified by the chat_id;
User: it represents a user and is managed automatically by Django authentication system. It has a unique email and a password;
House: it models an house where the system is installed. It’s described by the address and the street number and it is associated with a User object which represents the owner of the house;
Window: it is a generic window object, each one is associated with a house and has a current state (closed or open), a text description, a device name (identifier for the Arduino that manages this specific window) and a pin (the pin number connected to the actuator in the Arduino board), a timeout (a boolean field which says if the window can be moved autonomously by the system or not) and finally a date which represents the last_change timestamp.

## Slide 23: OpenWeather APIs
The data retrieved from the OpenWeather APIs are the current temperature and weather condition: the latter is categorized with different codes, each of them assigned to a close/open/ambiguous condition in order to process the information and take the correct decision. These are the categories:
Group 2xx: thunderstorm, we consider it as a close condition;
Group 3xx: drizzle, we consider it as an ambiguous condition;
Group 5xx: rain, we consider it as a close condition;
Group 6xx: snow, we consider it as a close condition;
Group 7xx: atmosphere, we consider it as an open condition;
Value 800: clear, we consider it as an open condition;
Group 80x: clouds, we consider it as an ambiguous condition.

## Slide 24: Decision logic
The system decides to open or close the windows depending on the 4 parameters values: temperature, wind, lightness and weather condition. For each of them there are three ranges of possible values: one for the close condition, one for the open condition, and one for an ambiguous condition. The decision is taken as follows:
If at least 2 values belong to the open condition range, then open the windows;
If at least 3 values belong to the close condition range, then close the windows;
If none of the previous, then there is an ambiguous condition and a “neighbourhood control system” is used in order to take the best decision.

## Slide 25: Neighbourhood control
In case of ambiguous condition the engine looks at neighbours last actions and takes the decision based on these rules:
If at least 2 of the neighbours have opened the windows manually in the last hour and less than 2 have closed them, then the engine opens all the windows;
If at least 2 of the neighbours have closed the windows manually in the last hour and less than 2 have opened them, then the engine closes all the windows;
If none of the above, then the engine decides to do nothing because the condition is very uncertain.
It is important to notice that the engine consider only the manual actions of the neighbours and not the automatic actions taken by the system, making the assumption that if a user closes (resp. opens) his windows manually means that there are conditions to close (resp. open), so the system takes the same action for each house of the neighborhood.

## Slide 26: Reinforcement learning approach

## Slide 27: Vanilla Q-Learning
The “vanilla” Q-Learning uses a Q-table that maps a state-action pair to a Q-value (the maximum expected future reward) which the agent will learn.
As the agent tries out different actions at different states through trial and error, following an explorative policy, the agent learns each state-action pair’s expected reward and updates the Q-table with the new Q-value.
After an agent has learned the optimal Q-value of each state-action pair, the agent at state S has to choose the action A associated with the maximum Q-value following a greedy policy.

## Slide 28: Vanilla Q-Learning (1)
The Bellman Equation tells us how to update the Q-table after each step. In Q-Learning, the agent updates the current Q-value with the estimated optimal future reward computed taking the greedy action, while the next action performed is chosen using, for example, an epsilon-greedy policy.
S = the state
A = the action the agent takes (chosen, for example, with an epsilon-greedy policy)
a = the action used to update the Q-value at the current state S (chosen with a greedy policy)
R = the reward from taking action A
t = the time step
⍺ = the learning rate
ƛ = the discount factor which causes rewards to lose their value over time (higher immediate rewards)

## Slide 29: DQN
DQN (Deep Q-Learning Networks) is a family of model-free reinforcement learning algorithms in which a neural network replaces the Q-table and maps input states to (action, Q-value) pairs for each possible action.
When the number of possible states is huge, the amount of time required to explore each state to create the Q-table would be unrealistic. Therefore, we approximate the Q-values with a neural network.

## Slide 30: DQN (1)
To obtain a more stable training process, two networks are used: the target and the prediction network. The steps involved in a DQN algorithm become:
Preprocess and feed the state S to the DQN, which will return the Q-values of all possible actions in the state
Select an action A using, for example, the epsilon-greedy policy
Perform action A, move to a new state S’ and receive a reward R. We store this transition in a replay buffer as <S, A, R, S’>
Sample some random batches of transitions from the replay buffer and calculate the loss over the batch (MSE of the predicted Q-value and the target Q-value given by the Bellman Equation)
Perform gradient descent with respect to actual network parameters in order to minimize the loss
After every C iterations, copy actual prediction network weights to the target network weights
Repeat these steps for M episodes

## Slide 31: DQN implementation ideas
In our system, a state S is defined by a particular combination of the 4 parameters values.
The temperature parameter can assume values in the continuous domain (infinite values)
The light parameter can assume discrete values between 0 and 253
The wind parameter can assume discrete values between 0 and 253
The OpenWeather codes assume discrete values (they are hundreds)
The number of possible combinations (states) is huge: deep reinforcement learning is needed
We suggest using a DQN for each house, which gives in output, for a particular state, the action to be performed for all the windows of the house.

## Slide 32: DQN implementation ideas (1)
A positive reward R is given to the agent if the user likes the decision taken by the system given a specific state S, while a negative reward is assigned in the opposite case. If the user does not care about the decision or forgets to give a feedback, the reward is 0. The user’s feedback could be collected using the Telegram bot
An episode corresponds to a day, in which several actions can be performed. A training period of 1-2 months should be taken into account to allow the system to get accustomed to the user’s will and habits
Once the training phase is completed, when a particular state S is registered, the network with the trained weights takes the state (embedded in a vector) in input and gives in output all the possible actions (open / close) associated with a Q-value. The action with the highest Q-value (greedy policy) is finally performed