## Slide 1: Smart neighborhood system for shutters management
Baraldi Francesco, Pagliani Matteo

## Slide 2: Outline
Introduction
Architecture
Prototype specifications
Reinforcement learning ideas
Video Demo

## Slide 3: Introduction
Too lazy to close the shutters in case of a thunderstorm?
Do you often forget to close the shutters before falling asleep?
Or do your flowers need sunlight when you are on holiday away from home?
 This system is the answer for you! Our product automatically open or close the shutters of houses depending on weather conditions. Its scalability allows it to be used not only by you, but also by your neighbours, aiming to control the shutters of several houses in your neighborhood simultaneously.

## Slide 4: How to use
You don’t have to worry about anything, the system takes care of your house for you:
When specific weather conditions trigger our system, it will take a decision about closing or opening the shutters in total autonomy. You will be notified directly on your smartphone when a decision is taken, and you can feed back if you liked that decision or not, giving us the possibility to improve based on your habits! The system learns how to perfectly fit your needs
When you are away, you can always control the shutters remotely via web
Obviously, you can control the shutters manually thanks to specific buttons installed in your house
The system takes into account your neighbours action to make better decisions on your own windows

## Slide 5: Composition of the kit
The kit is composed by:
1 Internal Kit per house: a microcontroller, an actuator and a button for each of the windows you want to control
1 External Kit per neighborhood: some sensors (a photoresistor and a wind speed sensor) and a control unit for the whole neighborhood, which will be installed in a strategic position close to the houses to be managed
Finally you shall install the Telegram application on your smartphone and keep on hand the web site for optimal control.

## Slide 6: Key points: why chosing us?
Because the system is:
Easy to setup
Not invasive
Automatic
Flexible
Scalable
Adaptive to users’ habits

## Slide 7: Architecture: real model

## Slide 8: Architecture: prototype

## Slide 9: Real model vs prototype
Real Model | Prototype
1 Arduino Nano for each window | 1 Arduino UNO Rev.3 for two windows
1 Raspberry Pi for each house which manages all the house’s windows and runs the internal bridge | Laptop as internal bridge
1 Raspberry Pi for each neighborhood that runs the external bridge | Laptop as external birdge
Server Django and engine hosted with a public IP | Server Django and engine running in localhost
Prettier buttons | Push buttons
1 custom actuator for each window | 1 servomotor for each window (Hitec and TowerPro)
Wind speed sensor | 1 potentiometer as wind speed sensor
Proper web app frontend for improved UE | Simple web app using Django template
Reinforcement Learning approach | Neighbours “control” in case of uncertainty

## Slide 10: Prototype specifications
Connection schemas, sensors and actuators
FSM for push buttons
Servo logic
Communication Protocols (Serial, HTTP e MQTT) and messages structure
Bridges
Web App and Django stuff
Telegram Bot
DB Sqlite structure
OpenWeather API
Neighbours dependency in case of uncertainty

## Slide 11: Connection schemas
The Arduino Uno for the internal kit is connected to:
1 Hitec servomotor
1 TowerPro servomotor
2 push buttons

## Slide 12: Connection schemas (1)
The Arduino Uno for the external kit is connected to:
1 photoresistor
1 potentiometer

## Slide 13: FSM for push buttons
States: {S0, S1, S2}
  S0: initial state
  S1: button pressed
  S2: button pressed more than one time consecutively
Inputs: {PRESSED, RELEASED}
  PRESSED : high (5V) digital signal due to the button pression
  RELEASED : low (0V) digital signal due to the button release
Outputs: {MOVE, NOT_MOVE}
  MOVE: allows the servos to change the state of the window (from open to closed or viceversa)
  NOT_MOVE: does not allow the servos to change the state of the window

## Slide 14: Code tables for serial communication
0xFF | 0x01 | WINDOW_PIN | 0xFE
Header | Payload length | Payload | Footer
Header (1 byte): identifies the beginning of the packet
Payload length (1 byte): specifies the byte length of the payload
Payload (1 byte): the microcontroller writes on the serial bus the number of the pin connected to the servomotor whose window has just changed state. The bridge will read from the serial and will update accordingly in the database the state of the window.
Footer (1 byte): identifies the end of the packet

## Slide 15: Code tables for serial communication (1)
0xFF | 0x02 | Potentiometer value | Photoresistor value | 0xFE
Header | Payload length | Payload | Payload | Footer
Header (1 byte): identifies the beginning of the packet
Payload length (1 bytes): specifies the byte length of the payload
Payload (2 byte): the first and the second byte are respectively the value read by the potentiometer and the value read by the photoresistor, both mapped from the original range 0 – 1024, to the range 0 – 253 in order to store them in exactly one byte
Footer (1 byte): identifies the end of the packet

## Slide 16: Web App
screenshot

## Slide 17: DB SqLite3

## Slide 18: DB SqLite3 (1)
The database is managed automatically by Django using the model part of the MVC approach: we define a python class for each table of the db and Django creates the respective relational db. The 4 classes are described below:
ChatTelegram: represents a chat telegram of users identified by the chat_id;
User: represent a user of the system and it’s the class managed automatically by the Django authentication system, it has a unique email and a password;
House: it models an house where is installed the smart-neighborhood system, it’s described by the address and the street number and has a User object associated which represent the owner of the house;
Window: it is a generic window object, each one assiocated to a house and has a current state (closed or open), a text description, a device name (identifier of arduino that manages this specific window) and a pin (pin connected to the actuator in the arduino board), a timeout, a boolean field which says if the window can be moved autonomously by the system or not, and finally a date which represents the last_change timestamp.

## Slide 19: OpenWeather codes
The data retrieved from the OpenWeather APIs are the temperature and the weather condition, the latter is categorized in different codes, we assigned each of them to a close/open/ambiguous condition in order to process the information and take the correct decision:
Group 2xx: thunderstorm, we consider it as a close condition;
Group 3xx: drizzle, we consider it as an ambiguous condition;
Group 5xx: rain, we consider it as a close condition;
Group 6xx: snow, we consider it as a close condition;
Group 7xx: atmosphere, we consider it as an open condition;
Value 800: clear, we consider it as an open condition;
Group 80x: clouds, we consider it as an ambiguous condition.

## Slide 20: Extra: Reinforcement Learning predictions with DQN
DQN (Deep Q-Learning Networks) is a model-free reinforcement learning algorithm. Model free RL algorithms don’t learn a model of their environment’s transition function to make predictions of future states and rewards.

## Slide 21: Vanilla Q-Learning
The vanilla Q-Learning uses a Q-table, a simple data structure that we use to keep track of the states, actions, and their expected rewards. More specifically, the Q-table maps a state-action pair to a Q-value (the estimated optimal future value) which the agent will learn. At the start of the Q-Learning algorithm, the Q-table is initialized to all zeros indicating that the agent doesn’t know anything about the world. As the agent tries out different actions at different states through trial and error, the agent learns each state-action pair’s expected reward and updates the Q-table with the new Q-value. Using trial and error to learn about the world is called Exploration.
The Q-Value is the maximum expected reward an agent can reach by taking a given action A from the state S. After an agent has learned the Q-value of each state-action pair, the agent at state S maximizes its expected reward by choosing the action A with the highest expected reward. Explicitly choosing the best known action at a state is called Exploitation.

## Slide 22: Vanilla Q-Learning (1)
A common strategy for tackling the exploration-exploitation tradeoff is the Epsilon Greedy Exploration Strategy.
At every time step when it’s time to choose an action, roll a dice
If the dice has a probability less than epsilon, choose a random action
Otherwise take the best known action at the agent’s current state
Note that at the beginning of the algorithm, every step the agent takes will be random which is useful to help the agent learn about the environment it’s in. As the agent takes more and more steps, the value of epsilon decreases and the agent starts to try existing known good actions more and more. Note that epsilon is initialized to 1 meaning every step is random at the start. Near the end of the training process, the agent will be exploring much less and exploiting much more.

## Slide 23: Vanilla Q-Learning (2)
The Bellman Equation tells us how to update our Q-table after each step we take. To summarize this equation, the agent updates the current perceived value with the estimated optimal future reward which assumes that the agent takes the best current known action. In an implementation, the agent will search through all the actions for a particular state and choose the state-action pair with the highest corresponding Q-value.
S = the State or Observation
A = the Action the agent takes
R = the Reward from taking an Action
t = the time step
Ɑ = the Learning Rate
ƛ = the discount factor which causes rewards to lose their value over time so more immediate rewards are valued more highly

## Slide 24: DQN
Deep Q-Learning: A Neural Network maps input states to (action, Q-value) pairs
Initialize your Main and Target neural networks
Choose an action using the Epsilon-Greedy Exploration Strategy
Update your network weights using the Bellman Equation

## Slide 25: DQN (1)
The learning process uses 2 neural networks. These networks have the same architecture but different weights. Every N steps, the weights from the main network are copied to the target network. Using both of these networks leads to more stability in the learning process and helps the algorithm to learn more effectively. In our implementation, the main network weights replace the target network weights every 100 steps.
The main and target neural networks map input states to an (action, q-value) pair. In this case, each output node (representing an action) contains the action’s q-value as a floating point number. Note that the output nodes do not represent a probability distribution so they will not add up to 1. For the example above, one action has a Q-value of 8 and the other action has a Q-value of 5.

## Slide 26: DQN implementation ideas

## Slide 27: Video DEMO?